## Slide 1: MEAD Making 101
Good mead comes from good honey

## Slide 2: History
Mead is an alcoholic beverage produced by the fermentation of a diluted mixture of honey and water.
Documented over 6,000 years ago. It is typically clear with a slight gold tint, with an alcohol content of between 7-22%.
By varying the proportions of honey and water and the point at which fermentation is stopped, a wide variety of types can be produced ranging from a very dry and light mead similar to more traditional white grape wines, to sweet and heavy-bodied desert wine.

## Slide 3: Importance of sanitization
All equipment used needs to be sanitized completely. Brew supply stores sell various products to kill off any unwanted yeast or bacteria.
Clean it all in a clean area, wash hands and rinse in warm to hot water often.
Once clean, watch that you are putting it in a clean place- don’t let it get contaminated.

## Slide 4: Yeasts already in Honey
Wild fermentations produce will unpredictable results
Best practices are to control the fermentation process
Use a known yeast for known results
Need to remove unwanted yeast or bacteria from the honey

## Slide 5: Using heat to kill unwanted yeast
The actual time required to kill yeast is 22 minutes at 140 F, and drops well below 5 minutes at 150 F and above.
Using temps in the 145 F range will preserve many of the aroma compounds
High temps change the character of the honey
Higher temps start to caramelize the honey

## Slide 6: Using Sulfites to kill unwanted yeast
The use of Sulfites to produce quality meads has the advantage of ease and lack of heating
No heating to cause shifts in flavors
The minimum threshold for adequate sanitation is 70 ppm, which equates to 0.4 grams per gallon at pH 3.5
some people are sensitive to these compounds
addition requires both an accurate scale and an accurate pH meter

## Slide 7: Sulfites… continued
Another disadvantage is that the proteins are not removed and the meads may require more time or fining to clarify
The pH of the must effects the amount of free SO2 present
Each Campden tablet contains 0.44 grams of sulfite (SO2)
Normal to use 1 Campden tablet per gallon

## Slide 8: Basics of fermentation
Ethanol fermentation, also called alcoholic fermentation, is a biological process which converts sugars such as glucose, fructose, and sucrose into cellular energy, producing ethanol and carbon dioxide as by-products. This is because yeasts perform this conversion in the absence of oxygen, alcoholic fermentation is considered an anaerobic process

## Slide 9: Fermentation
Fermentation does not require oxygen. If oxygen is present, some species of yeast (e.g., Kluyveromyces lactis or Kluyveromyces lipolytica) will oxidize pyruvate completely to carbon dioxide and water in a process called cellular respiration. This phenomenon is known as the Pasteur effect.
However, many yeasts such as the commonly used yeast Saccharomyces cerevisiae under certain conditions, ferment rather than respire even in the presence of oxygen. In wine making this is known as the counter-Pasteur effect. These yeasts will produce ethanol even under aerobic conditions, if they are provided with the right kind of nutrition.

## Slide 10: Fermenting mead
Mead fermentations are notoriously for taking a long time to reach completion
proper selection of yeast strains, agitation during fermentation, yeast nutrition and control of pH can dramatically increase the fermentation rate
single most significant factor effecting the rate of mead fermentation is yeast health
Yeast hydration is important to starting healthy cells
ensured by providing adequate nutrients in the form of yeast energizer and yeast nutrients

## Slide 11: The Honey
A tremendous part of the character of mead is derived from the honey
Honey contains, in addition to a rather complex mixture of sugars, enzymes, proteins, organic compounds and trace minerals
these interesting compounds give honey its distinctive flavor and characteristic aromas
Many of these are carried over into a mead

## Slide 12: Yeasts
A large number of yeasts are now available to the small scale mead maker
Most wine yeast strains will perform nicely
There are several commercial sources for high quality mead yeasts
Each yeast strain will add it’s own character to the mead
Yeasts will limit the potential alcohol content

## Slide 13: Yeast for Mead
Three important types of yeasts (from the point of view of their utilization, not from the point of view of biologists' nomenclature): baker's yeast, beer yeast and wine yeast.
Some people (a minority) use beer yeast to make mead. They are of two kinds: ale (saccharomyces cerevisiae) and lager (saccharomyces uvarum).
Most wine yeasts are also saccharomyces cerevisiae
Champagne yeasts are saccharomyces bayanus

## Slide 14: Forms of yeast
These yeasts come in two forms
5 g packages of dry yeast (cheap)
yeasts in liquid form much more expensive but supposed to be purer
Liquid forms of yeast harder to find
Yeasts will give different flavors but they will also lead to different alcohol contents and different quantities of residual sugar

## Slide 15: Yeast Hydration
dried yeast is common form
a yeast rehydration nutrient will help the yeast get off to a good start
GoFerm is a relatively widely available version of a rehydration agent. With GoFerm you use 1.25 times by weight of the yeast, 5 grams of GoFerm for a 4 gram packet of dried yeast.
Follow the package directions
The manufacture has tested for the best rehydration results, pay attention to temps
Follow the package directions

## Slide 16: Common yeasts used for Mead
Red Star’s Cote de Blanc - a champagne yeast with a high alcohol tolerance (Ron & Cameron’s fav for high alcohol)
Lalvin D-47 pretty good and best for medium to sweet meads. Medium Fermentation Speed, Low Alcohol Tolerance. - ICV-D-47 produces fewer esters and more earthy tones, which are good for dry mead and cider that is being considered for aging on leas and perhaps in oak
D-47 - another take: Lalvin ICV D-47 makes a nice crisp mead that leaves a nice white zinfandel character. It yields chardonnay buttery flavors and is good for cysers. Be sure to supplement with yeast nutrients, especially usable nitrogen. 14% Alcohol Tol. Fermentation temp 59-69f Moderate speed
Lalvin K1V, which is a fast starting, intermediate finishing wine yeast
Lalvin K1V-1116 produces a more "light and fruity" product.
Lalvin EC1118 High Alcohol, Fast Fermenter. Kills other yeasts – Our second choice
Lalvin 71B-1122 ferments quickly and completely in a wide range of temperatures. It is capable of metabolizing high amounts of malic acid and produces a smooth, aromatic meads that age quickly

## Slide 17: Water
Distilled water would have no minerals to help yeast
Spring water includes minerals and could add character to the mead
Unfiltered tap water will likely have tastes and characteristics unwanted in the mead.

## Slide 18: Putting it all together
Water, honey and yeast…. Does not include everything the yeast need to grow
Yeasts need nutrients to grow, particularly nitrogen in a form the yeast can use
Follow a recipe your first couple batches
Experiment with honey and yeast combinations – following a recipe
Meads need to have a “balance”

## Slide 19: Basic Mead Making Equipment
Stainless Steel Kettle (2.5 gallons or larger)
Fermenting Bucket
Carboy
Air lock
Racking Cane & Tubing
Thermometer
Hydrometer
Sanitizer
Brewing Instructions, Recipe or Book
Log or record book( or file)
Bottle Corker, Bottle Filler, Bottle Brush,
Bottles and corks

## Slide 20: Traditional Mead - Basic
INGREDIENTS for each gallon of mead to be made:
2 1/2 to 3 lbs. unprocessed honey (dry to semi-sweet)
Water to one gallon (Specific Gravity - 1.085 - 1.105)
1 tsp. Super Ferment (or 2 tsp. regular "nutrient")
2 tsp. acid blend (or 3/4 tsp. tartaric acid & 1 1/4 tsp. malic acid)
1/4 tsp grape tannin
1 campden tablet* (crushed - or substitute 1/8 tsp. sodium/potassium metabisulfite)
1 pkg. yeast

## Slide 21: PROCEDURE:
1. Mix all the ingredients EXCEPT the yeast and the campden tablet. Stir the must until the honey and additives are completely dissolved. Cover the pail to keep out dust and air.
2. Crush and dissolve the campden tablet in 1 oz. of warm water. Add this to the must and stir well. Cover the pail. Let the must stand for one day, stirring several times. *ALTERNATIVE: Heat honey with an equal volume of water to 145°F and let stand for 15 minutes to pasteurize. (DO NOT BOIL!) Cool and add remainder of water before proceeding to next step.
3. Rehydrate the dried yeast by sprinkling it into 1/2 cup water( water at the temp per the package) in a sanitized jar and cover for 20 minutes. KEEP an eye on it!
Add the yeast "slurry "/starter to mixture. Re-cover the primary fermenter and allow primary fermentation to proceed for 5-7 days or until foaming subsides.
Add air lock and keep in a cool place. Temps will effect flavors, especially in primary fermentation
4. Syphon the mead into a sterile glass jug. Avoid the transfer of sediment and aeration as much as possible. Be sure the mead completely fills the jug - into the neck. Attach a fermentation lock and allow the fermentation to go to completion (.995 - 1.020 S.G.) – this stage is known as Secondary Fermentation, temps are not as important

## Slide 22: Waiting….
Air locks offer the fair way to monitor primary fermentation
Primary is complete when bubbles slow to one every minute or two
A Hydrometer is one of the best ways to monitor true progress of fermentation
Using starting gravity minus current Specific Gravity(SG) you can calculate the alcohol content
Keep records. Keep records
Spread sheet can calculate for you
FaceBook: Gulf Coast Mead Festival and look in “files” for a good record sheet (Excel with drop down menues)

## Slide 23: Racking
Process of transferring mead from one container to another
Follow strict sanitation of ALL equipment that touches the mead: hoses, racking cane, thermometer, hydrometer, spoons, hands etc.
Avoid aeration
Don’t transfer sediment (lees)
Clarification can happen quickly or take time
Don’t be afraid of sampling
Please let it age…. In a cool place!
Many off flavors will age out – ask about my cyser.

## Slide 24: Back sweetening
Brings a mead up to a sweetness you want
Flavor will differ from making the mead with residual sugars (fermentation effects flavors)
Could kick off fermentation again, so stabilize first (next slide)
Be sure to pasteurize honey before adding (heat or sulfite)
Warm/heat honey and water(or some of the mead) in a 1:1 ratio until fully dissolved
Add warm mixture slowly with lots of stirring and taste along the way.

## Slide 25: Bottling
After racking and aging…
Crush, dissolve and add 1/2 Campden tablet per gallon to the mead. Allow the mead to stand for one month in a cool dark place to stabilize
repeat "racking" process until clear
The mead may be sweetened to taste with additional honey, if desired, after stabilization (1/2 tsp. potassium sorbate & 1/2 campden tablet per gallon)
Bottling without stabilizing a mead can create a “bottle bomb”

## Slide 26: Common Mead Types:
Acerglyn — A mead made with honey and maple syrup.
Bochet — the honey is caramelized or burned separately before adding the water. Gives toffee, chocolate, marshmallow flavors.
Braggot — Originally brewed with honey and hops, later with honey and malt — with or without hops added. Welsh origin
Cyser — A blend of honey and apple juice fermented together; see also cider.
Hydromel — Hydromel literally means "water-honey" in Greek. It is also used as a name for a very light or low-alcohol mead.
Melomel — Melomel is made from honey and any fruit.
Metheglin — Metheglin starts with traditional mead but has herbs and/or spices added. Akin to mulled wine or Wassell.
Pyment — Pyment blends honey and red or white grapes. Pyment made with white grape juice is sometimes called "white mead."
Sack mead — This refers to mead that is made with more honey than is typically used.
Short mead — Also called "quick mead." A type of mead recipe that is meant to age quickly, for immediate consumption.
There are MANY more names for types of mead, the above are commonly used

## Slide 27: Reference files for todays class
FaceBook: Gulf Coast Mead Festival – see files section
www.gulfcoastmeadfest.com look on right side under Activities
April 25th 2020 is the next Gulf Coast Mead Festival

## Slide 28: Q&A
Fruits or other addition before or after primary fermentation?
Air space…..
Types and variations….
Fining agents…. +/- ions
NOTE: ALL EQUIPMENT SHOULD BE WELL WASHED AND STERILIZED WITH A SOLUTION OF SODIUM METABISULPHITE. FERMENTATION TEMPERATURES SHOULD BE NO LOWER THAN 60 DEGREES F. OR HIGHER THAN 80(or70)° F